US-020  Ultrasonic Module

1.Sketch out

This US-020 ultrasonic module can realize 2 ~ 700cm of non-contact ranging function, has 5 V of wide voltage input range, static power consumption is less than 3mA. Their own temperature sensor will revise the ranging and has many communication modes like GPIO, just like watchdog inside, very stable and reliable.

2.Technical parameters

| Electric parameter | US-020 Ultrasonic Module |
| --- | --- |
| working voltage | DC 5V |
| quiescent current | 3mA |
| operating temperature | 0~70℃ |
| output mode | GPIO |
| detection angle | <15° |
| detection range | 2cm-700cm |
| detecting precision | 0.3cm+1% |

3.Pictures and Size

The size of the module:45mm*20mm*1.6mm,there are two Mechanical hole on it.

US-020  dimension figure

4.Interface specifier

This module have an port:4 Pin Power supply and communication interface

Four pins from left to right ,they are defined as follow :

1.NO.1 pin:Connected to VCC(DC 5V)

2.NO.2 pin: Connected to MCU’s Trig port,

3. NO.3 pin: Connected to MCU’s Echo port

4. NO.4 pin:Connected to GND

5. Operating principle

- US-020 sequence chart

We only need to produce a high leve signal over 10us,the module can produce  eight 40KHZ Ultrasonic pules,than chack the respond signal,when there is a respond signal,Echo port will output a signal.

We can calculate the distance though the time Echo keeps high leve signal,that is to say distance=(time*340)/2